## Slide 1
Lab #5
ASIC Backend Flow
ECE4810J System-on-Chip Design
Yihua Liu
UM-SJTU Joint Institute
ayka_tsuzuki@sjtu.edu.cn
Oct. 31, 2022

## Slide 2
Overview
Overview
ASIC Flow Front-End vs Back-End
VLSI Design Methodologies
Productive MLM & VLSI Design
PyMTL3
Reference

## Slide 3
ASIC Flow Front-End vs Back-End
Front-End:
Hardware modeling in HDL
Synopsys VCS for 4-State RTL Simulation
Synopsys Design Compiler for Synthesis
Synopsys VCS for Fast-Functional Gate-Level Simulation
Back-End:
Synopsys PrimeTime for Post-Synth Power Analysis
Synopsys IC Compiler/Cadence Innovus for Place-and-Route
Synopsys VCS for Back-Annotated Fast-Functional GL Simulation
Synopsys PrimeTime for STA & Performing Hold Fixing
Synopsys PrimeTime for Post-Place-and-Route Power Analysis
Problem
Solution Specification
Behavioral Representation
RTL Coding
VHDL/Verilog
Functional Verification
Verification Succeeded?
No
Back End
Yes
Synthesis
Synthesis Verification
Verification OK?
No
Place & Route
Parasitic Extraction
STA
Timing OK?
Yes
Post-layout Verification
Verification OK?
No
Yes
The End
No
Yes
Notes: Mixed modeling

## Slide 4
VLSI Design Methodologies
HPF
Hardware Preprocessing Framework
DUT
TB
DUT’
Sim
TB’
Mixed
(Verilog+Perl)
HDL (Verilog)
gen
FPGA/ASIC
synth
gen
HGF
Hardware Generation Framework
DUT
TB
DUT’
Sim
Host Language
(Scala)
HDL (Verilog)
gen
FPGA/ASIC
synth
gen
TB’
TB
HDL
Hardware Description Language
DUT
Sim
TB’
HDL (Verilog)
FPGA/ASIC
synth
Fast edit-sim-debug loop
Single language for
structural, behavioral, + TB
Difficult to create highly
parameterized generators
Slower edit-sim-debug loop
Multiple languages create
"semantic gap"
Easier to create highly
parameterized generators
Slower edit-sim-debug loop
Single language for
structural, behavioral, + TB
Easier to create highly
parameterized generators
Cannot use power of host
language for verification

## Slide 5
Productive MLM & VLSI Design
Multi-Level Modeling
SystemC
VLSI Design
Chisel
HGSF
Hardware Generation and Simulation Framework
DUT
Sim
TB
DUT’
Sim
Host Language
(Python)
HDL (Verilog)
gen
cosim
FPGA/ASIC
synth
Single framework for ML
modeling & VLSI design
Fast edit-sim-debug loop
Single language for
structural, behavioral, + TB
Easy to create highly
parameterized generators
Use power of host
language for verification

## Slide 6
PyMTL3 Framework
Test & Sim Harnesses
Model
Config
Elaboration
PyMTL Domain Specific Language (Python)
Model Instance
Simulation Pass
Translation Pass
Analysis Pass
Transform Pass
Simulatable Model
System Verilog
Analysis Output
New
Model
PyMTL In-Memory Intermediate Representation (Python)
PyMTL Passes (Python)

## Slide 7
PyMTL/Verilog Integration
Verilog Source
Verilator
RTL/C++ Source
C Interface Source
Translation
LLVM/GCC
Wrapper Gen
C Shared Library
Translation Cache
SimJIT-RTL Tool
PyMTL
RTL Model Instance
PyMTL
CFFI Model Instance

## Slide 8
PyMTL3: Levels of Abstraction
PyMTL3 hardware modeling framework can be used for functional-level modeling, verification, and simulator harnesses. Computer architects can model systems at various levels of abstraction including at the: functional-level (FL), cycle-level (CL), and register-transfer-level (RTL). Functional-Level – FL models implement the functionality but not the timing of the hardware target. FL models are useful for exploring algorithms, performing fast emulation of hardware targets, and creating golden models for verification of CL and RTL models. FL models can also be used for
building sophisticated test harnesses. FL models are usually the easiest to construct, but also the least accurate with respect to the target hardware.
Cycle-Level – CL models capture the cycle-approximate behavior of a hardware target. CL models will often augment the functional behavior with an additional timing model to track the performance of the hardware target in cycles. CL models are usually specifically designed to enable rapid design-space exploration of cycle-level performance across a range of microarchitectural design parameters. CL models attempt to strike a balance between accuracy, performance, and flexibility.
Register-Transfer-Level – RTL models are cycle-accurate, resource-accurate, and bit-accurate representations of hardware. RTL models are built for the purpose of verification and synthesis of specific hardware implementations. RTL models can be used to drive EDA toolflows for estimating area, energy, and timing. RTL models are usually the most tedious to construct, but also the most accurate with respect to the target hardware.

## Slide 9
PyMTL3: Synthesizability
Keep in mind that PyMTL3 is embedded within Python, which is a fully general-purpose language. Given this, it is very easy to write PyMTL3 code that does not actually model any kind of realistic hardware. Students must be very diligent in actively deciding whether or not they are writing synthesizable RTL models or non-synthesizable code. Students must always keep in mind what hardware they are modeling and how they are modeling it!
Concurrent blocks: model hardware update_ff, update, update_once, accept non-synthesizable code only for debugging, assertions, or line tracing
Elaboration code: outside concurrent blocks, generate hardware, accept any code
Always allowed | Allowed with Limitations | Explicitly not Allowed
Bits bitstruct | accessing Python lists | / // % ** += -= *= /= %= **= //=
& ¦ ^ ~ + - >> << | writing signals | and or not while break continue
== != > >= < <= | writing temporary variables | def global class try except raise
reduce_and() reduce_or() reduce_xor() if else elif | reading reset signal | as is in with return yield import from del exec pass lambda finally
sext() zext() concat() | read-modify-write signal | constructing Python lists/dicts, using dicts
s.signal[n] s.signal[n:m] | * | reading/writing non-signals/clk signal
reading constvars/signals | for | writing reset signal
Instances of InPort, OutPort, or Wire
Must use <<= in update_ff
Must use @= in update
Can synthesize into quite a bit of logic
with statically known bounds
Must use <<= in update_ff
Must use @= in update
only in (sync) update_ff
not in (async) update
Use & | ~ instead
read-modify-write
not currently supported

## Slide 10
PyMTL3 Basics
% python
>>> from pymtl3 import *
Bits and Bitstruct Data Type
Most HDLs support four-state values (0, 1, X, Z)
PyMTL3 supports two-state values (0, 1)
Bits1, Bits2,…, Bits255
>>> a = Bits32( 0xabcd0123 )
>>> a[24:32] = 0x67
>>> b = Bits32( a )
>>> a = Bits8( 0b10101100 )
>>> reduce_and(a)
Bits1(0x0)
>>> a = Bits8( 0xab )
>>> b = Bits12( 0xcde )
>>> concat( a, b )
Bits20(0xabcde)
>>> a = Bits4( 0xa )
>>> sext( a, 8 )
Bits8(0xfa)
>>> zext( a, 8 )
Bits8(0x0a)
>>> a = Bits8( 0xff )
>>> trunc( a, 3 )
Bits3(0x7)
>>> @bitstruct
... class Point:
... x: Bits4
... y: Bits4
...
>>> pt1 = Point(3, 4)
>>> pt1
Point(Bits4(0x3),Bits4(0x4))
>>> str(pt1)
'3:4'
>>> pt1.x
Bits4(0x3)
>>> pt1.to_bits()
Bits8(0x34)
>>> Point.from_bits( Bits8(0x34) )
Point(Bits4(0x3),Bits4(0x4))
>>> nbits = 8
>>> PointN = mk_bitstruct( f"Point{nbits}", {
... 'x': mk_bits(nbits),
... 'y': mk_bits(nbits),
... })
...
>>> pt2 = PointN( 3, 4 )
>>> pt2
Point8(Bits8(0x03),Bits8(0x04))
>>> pt2.to_bits()
Bits16(0x0304)

## Slide 11
Reference
University of Porto. “desing_flow_LuisGomes_v1.” Mar. 2022.
Christopher Batten. “ASIC Flow Front-End.” 2022.